## Slide 1: The computer system
Introduction to computers FDN 1202

## Slide 2: A typical computer

## Slide 3: Components of a Computer
All types of computers follow a same basic logical structure and perform the following five basic operations for converting raw data into information useful to their users.

## Slide 4: Functions of a Computer

## Slide 5: Basic Components of a Computer

## Slide 6: Input unit
This unit contains devices with the help of which we enter data into computer.
This unit makes link between user and computer.
The input devices translate the information into the form understandable by computer.

## Slide 7: Storage Devices
Components which allow data to be stored within a computer system.
This includes devices such as hard disk drives and compact drives.

## Slide 8: Output unit
Consists of devices with the help of which we get information from computer.
This unit is a link between computer and users.
Output devices translate the computer’s output into the form which can be understand by users.

## Slide 9: CPU Functions
Fetch instructions.
  CPU must read instructions from memory.
Interpret instructions.
  Instructions must be decoded to determine what action is required.
Fetch data.
  Execution of an instruction may require reading data from memory of an IO module.
Process data.
  Execution of an instruction may require performing some arithmetic or logical operation on data.
Write data.
  Results of an instruction execution mayrequire writing data to memory or an IO module.

## Slide 10: Main Components of the CPU
Control Unit(CU)
  Controls the operation of the CPU and hence the computer.
Arithmetic and Logic Unit (ALU)
  Performs computer’s data processing functions.
Registers
  Provides storage internal to the CPU.
  High speed memory locations.
CPU Interconnections(BUS)
  Some mechanism that provides for communication among the control unit, ALU and registers.

## Slide 11: Simplified view of a cpu

## Slide 12: Internal Structure of the CPU

## Slide 13: ALU (Arithmetic Logic Unit)
This unit consists of two sub sections namely
  Arithmetic Section
    Perform arithmetic operations like addition, subtraction, multiplication and division. All complex operations are done by making repetitive use of above operations.
  Logic section
    Perform logical operations such as comparing, selecting, matching and merging of data.

## Slide 14: Control Unit
This unit controls the operation of all parts of computer but does not carry out any actual data processing operations.
Functions of this unit are:
  It is responsible for controlling the transfer of data and instructions among other units of a computer.
  It manage and coordinated all the units of the computer.
  It obtains the instructions from the memory, interprets them, and directs the operation of the computer.
  It communicates with Input/output devices for transfer of data or results from storage.
  It does not process or store data.

## Slide 15: CPU Registers
CPU needs to store instructions and data temporarily while an instruction is being executed.
  To remember the location of the last instruction.
  To remember the location of the next instruction.
  To hold the operands and results.
CPU needs a small internal memory.
Called Registers.
  Set of storage locations.
  Faster, Smaller and more expensive.
  Number ad function vary between processor designs.

## Slide 16: System Interconnections
Bus
  Communication pathway connecting two or more devices.
  Shared transmission (transportation) media.
    Multiple devices are connected to a bus.
    Only one device an transmit data at a time.
  A group of parallel wires.
    Each wire in a bus can transfer one bit of information.
    The number of parallel wires in a bus is equal to the word length of a computer (8 bits, 16 bits, 32 bits, 64 bits)
    Bus can transfer word of information at a time

## Slide 17: System interconnections

## Slide 18: System bus
Computer system contain a number of different buses.
A bus that connects major components (CPU, Memory, I/O) is called a System Bus.
On any bus, the lines can be classified into three functional groups.
Data Lines (Data Bus)
Address Lines(Address Bus)
Control Lines(Control Bus)

## Slide 19: Data bus
Provide a path for moving data between system modules.
No difference between “data” and “instruction” at this level.
The data bus typically consists of 6,16,or 32 separate lines.
Each line carry only 1 bit at a time, the number of lines determine how may bits can transferred at a time–overall system performance.
Width is a key determinant of performance. (Width = Number of lines.)

## Slide 20: Address bus
Identify the source or destination of data on the data bus.
Bus width determines maximum memory capacity of the system.
  E.g. 8080 has 16 bit address bus giving 64k address space (memory size)
Also used to address I/O ports.

## Slide 21: Control bus
Used to control the use of data and address bus.
As a shared transmission medium.
  E.g. Bus Request, Bus Grant etc.
Transfers control and timing information
  Memory read/write signal.
  Interrupt request.
  Clock signals.
  I/O read write.

## Slide 22: Instruction set
Instruction Set is the complete collection of different instructions that are understood by a CPU.
Different Instruction Sets for different CPU designs.
A large part of the CPU design involves implementing the machine instruction set, referred to as Processor’s Instruction Set.

## Slide 23: Instruction set
Instructions are
Machine Codes.
Binary Numbers(Stored in the Memory)
Usually represented by assembly codes.

## Slide 24: Instruction set
In machine code each instruction has a unique bit pattern.
  E.g.1010100010100011
For human use, a symbolic representation is used.
  E.g. ADD, SUB, LOAD
Operands can also be represented in the same way.
  E.g. ADD A, B

## Slide 25: Instruction set
Each instruction must contain four basic pieces of information.
  Operation Code (OpCode)
    Operation to be performed (Do this)
    E.g. ADD, SUB, LOAD, STOR etc.
  Source Operand Reference
    Operands (inputs) for the operation (To this)
  Result Operand Reference
    Result of the operation (Put the answer here)
  Next Instruction Reference
    Next instruction to be fetched (When you have done that, do this...)

## Slide 26: Hardware
A generic term used to describe any component of a computer system with a physical presence and which can, therefore, been seen and touched.
Hardware components are often categorized as;
  Input
  Output
  Storage
Devices which are not an integral part of the CPU are referred to as peripherals.

## Slide 27: Input Devices
Text entry devices.
Positioning, pointing and drawing devices.
Scanning devices.
3Dinteraction devices

## Slide 28: Output devices
Following are few of the important output devices which are used in a computer.
  Monitors
  Speakers
  Printers